## Slide 1: COMBINE:Leveraging the power of wireless peers through Collaborative downloading
Ganesh A. et. al.

## Slide 2: Introduction
Mobile devices are equipped with multiple wireless network interfaces
  WLAN interaces.(802.11,Bluetooth)
  WWAN interfaces.(GPRS)
WLAN offers much higher speeds than WWAN

## Slide 3: COMBINE
A system for collaborative downloading that uses both WLAN and WWAN in combination in an attempt to bridge the range-speed dichotomy
Nodes in close vicinity use high speed WLAN to discover each other,form collaborative group and stripe traffic across the WWAN links.
  increases effective WAN download speed,

## Slide 4: Contributions
Cost modeling
  By contributing its WWAN bandwidth for the benefit of other peers, a node both monetary and energy cost which needs to be accounted for.
Accounting
  The cost computed forms the basis of a market wherein nodes buy and sell WWAN bandwidth resources. Need to keep track of the credits earned or debits incurred.
Collaboration group formation
Striping protocol
  a workload distribution algorithm to farm out work across the participants in the collaboration group

## Slide 5: Overview
Setting
  A requester seeks to utilize the WWAN links of one or more collaborators.
  A collaborator contributes its WWAN bandwidth only when it is not in use.
  need for incentives
Each collaborator estimates its cost of providing help and communicates it to the initiator.
Initiator compares the bids from the collaborators and chooses the best one and proceed to form a collaboration group.
  COMBINE includes accounting mechanism where initiator issues signed IOUs to the collaborators.

## Slide 6
Once a collaboration group is formed COMBINE uses a work-queue algorithm to distribute work across collaborators.
COMBINE uses HTTP byte-range requests to stripe traffic across multiple WAN links.

## Slide 7: Modeling cost
Appropriately model the cost of sharing bandwidth so that the offered price ishigh enough to compensate the collaborator but not high enough to be unattractive to the initiator.
Two principal costs that a collaborator incurs
  cost of transferring data on the WWAN link.
    depends on the tariff structure imposed by the service
  opportunity cost of expending battery energy on behalf of a peer

## Slide 8: Unifying monetary and energy cost
Both energy and money are valuable resources but are quantified in different units that need to be reconciled.
Opportunity cost would be lower for a user who is idling compared to a user who needs to use the device at any cost.
  modeled as the function of the fraction of battery energy remaining (BR)
Monetary cost (MC) of performing a data transfer is unified with the opportunity cost and toatal cost TC is expressed as MC/BR

## Slide 9: Estimating battery depletion
battery depletion (BD)
BD=(time_elapsed*BDt)+(bytes_sent_or_recd*BDd)
energy characteristics of WLAN and WWAN are likely to be different.
BD=(time_elapsed*BDt)+(bytes_sent_or_recdWLAN*BDd_WLAN)+(bytes_sent_or_recdWWAN*BDd_WWAN)

## Slide 10: Accounting
Requirements
  Storing credits
  Cheat-proof
  Privacy
  Flexibility
  Efficiency

## Slide 11: Accounting in COMBINE
Central authority
  issues public/private key pairs upon presentation of a proof of identity.
Accounting server
  keeps track of credits/debits accrued by each user.
If an initiator finds the a collaborator's bid to be acceptable,it initiates the process of having the collaborator download content for it
Initiator issues a signed note of credit termed an IOU
The collaborator transmits the IOUs to the accounting server for redemption.
IOU={keypub,amount,h(x),seq,exp,signkpriv}

## Slide 12: Group formation algorithm
Each node i periodically wakes up its WLAN card and broadcast I-am-alive message which includes-
  TCi- cost of downloading one unit of data
  Bi- WWAN speed it can offer
On receiving a an I-am-alive message the initiator responds with a CCHECK message containing-
  The URL of the file that needs to be downloaded
  The time after which it will reply to the node with a collaboration acknowledgement.
On receiving CCHECK, the device checks its local cache for the URL mentioned in the message and if it is there and up-to-date then it informs the initiator of the availability.
Initiator evaluates all the I-am-alive message and selects the group of collaborators.
Initiator sends out CACK message to all selected collaborators

## Slide 13: Group selection criteria
Assume the user wants to download a file of size F and he is willing to incur a cost of C to do so.
Threshold-based group selection:
  Initiator calculates TC' = C/F
  All nodes whose bids contain TC value less than TC' are selected and sorted in descending order and the first n nodes are selected.
Opportunistic group selection
  each collaborator i, working in parallel, downloads xi with bandwidth Bi
  Total ttime taken to download the file -
    max(x1/B1,x2/B2,....,xN/BN)

## Slide 14
Determine optimal values of xi, i=1....Nso as to minimize the total time subject to the constraints

## Slide 15: Work distribution
Work-Queue algorithm
  Initiator gets the total file size to be downloaded and forms a work queue with fixed equal size byte ranges of the file
  Collaborators query the initiator and pick up the next available item from the work-queue, download the amount of data as specified in its work-item and return it to the initiator.
  Each collaborator picks up more work when it is done with its current work item, and keeps working until the queue is empty.

## Slide 16
Opportunistic algorithm
  follows directly from the opportunistic group selection.
  rather than solve the optimization and compute the work allocation just once for the entire file, it is solved repeatedly over smaller partitions of the file.
  The initiator divides the file of size F into fixed-size partitions of size p bytes each and apportions to each partition a cost budget of (C/F )p

## Slide 17: Experimental evaluation
Group formation
  collaborators overload the SSID field of wi-fi beacons with cost and WWAN speed information
  initiator listens to I-am-alive beacons for 4 secs
  total time for group formation on average takes less than 8 secs.

## Slide 18: Optimal chunk size

## Slide 19: HTTP throughput and speed-up

## Slide 20: Work-queue vs Optimized work distribution

## Slide 21: Agility and adaptation

## Slide 23: Impact of cryptography
Elliptic curve digital security algorithm(ECDSA) has better performance than RSA for mobile systems.

## Slide 24: Estimation of battery depletion
estimate BDt and BDd using controlled calibration experiments.

## Slide 25: Discussion
Security
  issue of privacy
  issue of confidentiality
  ensuring authenticity
User interface
WWAN service providers