## Slide 1: Quality of Service (QoS)
IIT Kharagpur, Spring 2017
Amit Saha

## Slide 2: Menu
Why QoS
IntServ
DiffServ
  Policing and dropping
  Queuing/Scheduling
  Traffic Shaping
Active Queue Management (ECN)
Notes: Voice call – 64 kbps
Voice delay (max) – 300 ms

## Slide 3: References
Internet QoS – Architecture and Mechanisms for Quality of Service
  Zhang Wang
Presentations available on the internet
  QoS – Introduction to Quality of Service Concepts and Protocol – Peter R. Egli, Indigoo.com
  Fundamentals of Quality of Service - Gopan Govindan
  Quality of Service – Abhishek Wadhwa
  QoS – Sri Safrina
Various documentation on the internet
Notes: Voice call – 64 kbps
Voice delay (max) – 300 ms

## Slide 4: Why QoS?
Reliability
Delay
Jitter
Bandwidth
As you increase the capacity of any system to accommodate user demand, user demand will increase to consume system capacity.
A
B
10 Gbps
5 Gbps
6 Gbps
Notes: Voice call – 64 kbps
Voice delay (max) – 300 ms

## Slide 5
Delay Jitter
Maximum Delay
Average Delay

## Slide 6
Departure at source
Arrival at destination
Play out at destination
1
2
3
4
5
6
1
3
2
4
5
6
1
2
3
4
5
6
Delay Offset

## Slide 7: Application expectations
Latency and Fidelity (packet loss) – conflicting goals
Worst case delay = delay offset high fidelity but high latency!
Low delay Low latency but possibly low fidelity
Intolerant applications need absolute fidelity
Tolerant applications don’t need absolute fidelity

## Slide 8: Integrated Services (IntServ)
Explicit resource reservation along entire path
Needs every intermediate node to conform
Entirely decoupled from route selection

## Slide 9
QoS Routing Agent
Admission Control
Reservation Setup Agent
Resource Reservation Table
Flow Identification
Packet Scheduler
Control Plane
Data Plane

## Slide 10: Reservation Setup (RSVP)
R1
R2
R4
R3
S1
D1
D2
PATH Message
RESV message

## Slide 11: Admission Control
Allow new flow only if enough spare resources
  Need to monitor resources
Parameter based
  Difficult to specify exactly how much a flow will use
  Reduced resource utilization
Measurement based
  Statistical multiplexing
  Improved resource utilization

## Slide 12: Measurement based
New estimation = (1 – w) x old estimation + w x latest sample

## Slide 13: Flow Identification
5 tuple is the most common way of identifying a flow
Per-packet flow identification for a large number of flows challenging at wire speed

## Slide 14: Packet Scheduler
Most important step!
Enforces resource allocation
Also known as Queuing

## Slide 15: IntServ Services
Guaranteed Service
Controlled Load Service
But first,
  Flow specification
  Service specification

## Slide 16: IntServ: Flow Specification
Peak rate
Average rate
Burst size – sustained insertion at peak rate
Maps to leaky bucket

## Slide 17: Leaky Bucket

## Slide 18: Service Specification
Minimum bandwidth
Delay – average or worst case
Delay jitter
Loss rate

## Slide 19: Guaranteed Service
TSpec
  Bucket rate (r bytes/sec) – rate of token arrival
  Peak rate (p bytes/sec) – peak rate of packet arrival
  Bucket depth (b bytes)
  Minimum policed unit (m bytes) – any packet less than ’m’ bytes is counted as ’m’ bytes
  Maximum packet size (M bytes)
RSpec
  Service rate (R bytes/sec)
  Slack Term (S microseconds) – Extra delay that a node may add to still meet end-to-end delay requirements

## Slide 20: Controlled Load Service
TSpec only – no RSpec
  Bucket rate (r bytes/sec) – rate of token arrival
  Peak rate (p bytes/sec) – peak rate of packet arrival
  Bucket depth (b bytes)
  Minimum policed unit (m bytes) – any packet less than ’m’ bytes is counted as ’m’ bytes
  Maximum packet size (M bytes)

## Slide 21: What if sender is lying?
Policing
  Packets that do not conform to TSpec are treated as best effort and could be dropped
Shaping
  Buffer packets to conform to TSpec by buffering.
  Done in internal nodes and not at the edge

## Slide 22: Packet Scheduling/Queuing
FIFO
Priority Queue

## Slide 23: Queuing Techniques
Round Robin
Weighted Round Robin /
Class Based Queuing
Notes: What happens if there are no tokens and packet arrives?

## Slide 24: Weighted Fair Queuing

## Slide 25: IntServ Problems
Suited for long lived flows
  Video conferencing
  Most web flows are short lived
All intermediate network elements/routers must support IntServ
  Per-flow classification and scheduling
Authorization, authentication, and accounting of reservations “difficult”
Influenced DiifServ and MPLS

## Slide 26: DiffServ
Classify traffic into forwarding classes (and loss priority) – individual flows do not matter
Define forwarding behavior, not services
No resource reservation setup
Admission control at edge of network

## Slide 27: Forwarding Classes
Practically there is a many to one mapping from FC to Output Queues
Output port
FC1
FC2
FC3
FC4

## Slide 28
Customer network
Customer network
Customer network
Customer network
Boundary node; classifies and marks forwarding classes
Interior node; looks at forwarding class only – not quite true in reality

## Slide 29: Per-hop Behavior (PHB)
Externally observable forwarding treatment at a single node is PHB
All packets undergoing same PHB are called as a behavior aggregate

## Slide 30: Differentiated Services Fields

## Slide 31: IP Precedence

## Slide 32: DSCP
Redefines the IP TOS field and tries to maintain some backward compatibility

## Slide 34: Assured Forwarding (AF) PHB Group
Four forwarding classes and 3 drop priorities within each FC.
Drop priorities are used to select which packets to drop during congestion

## Slide 35: Example PHBs
Default PHB – RFC 2474 – DSCP 0 – traditional best-effort service (FIFO)
Class-selector PHB – RFC 2474 – backward compatibility with IP precedence – xxx000
Assured Forwarding PHB – RFC 2597 - 4 AF classes - AF1, AF2, AF3, AF4
Expedited Forwarding PHB – RFC 2598 – map to priority queue – DSCP 46

## Slide 36: QoS at Boundary Node – The model
Classifier
Marker
Meter
Remarker
Shaper
Dropper
Classification
Conditioning

## Slide 37: Classification at Boundary Node
Classifier
  BA Classifier – Classify based on DSCP code point in packet
  MultiField (MF) Classifier
Marker - actually sets the DSCP code point in the packet

## Slide 38: Conditioning at Boundary Node
Meter
  Token bucket
  Dual Token Bucket
Marker – Change the DSCP or mark non conformant packets for further action
Shaper – Ensure that the customer traffic follows certain rates
Dropper/Policer – Easier to implement than shaping since shaping needs buffering

## Slide 39: Traffic Policing
Dual Token Bucket for packet coloring
Also known as trTCM (Two-Rate Tri-Color Marker)
PIR: Peak Information Rate
PBS: Peak Burst Size
CIR: Committed Information Rate
CBS: Committed Burst Size

## Slide 40: trTCM

## Slide 41: RED
/ Tail drop

## Slide 42
RED
WRED

## Slide 43: Putting it all together

## Slide 44: Ingress Port
Input port
Classifier
Policer
red | yellow | green
FC LP
FC LP
Either BA or MF
Switching/Routing
Packet buffer for queues
Store packet in memory meant for appropriate Q

## Slide 45: Egress Port
Output port
Switching/Routing
Shaper
Dropper
Q1
Q2
FC LP
Scheduler
Packet buffer for queues